## Slide 1: CANoe PSM implementation
More Lives Saved
More Life Lived
Agapi Grigore
SWV

## Slide 2: Needed files:
1. PowerSupplyControl.cin → Functions for used for panel and CAPL tests
2.1 PSM.sysvar → System variables
2.2 Core_Functions_SysVar.vsysvar → System variables
3. PSM.can → Event (button) handlers
4. PowerSupplyPannel.xvp → Panel interface
5. PSM_StartValues.svc → Panel configuration
PTC location: e:/MKSProjects/SWVR_PP_CI_Activities/CANOE_TEST_PLATFORM/Includes/HW_Modules/PSM/
Implemented and tested on : CANoe Build 15.4.35 (SP4) – 64 bit

## Slide 3
1. PowerSupplyControl.cin
  If you wish to access PSM functionality through CAPL scripts, this must be included, otherwise skip this step.
    E.g., for DAIMLER MMA:
Note: If the core structure is used, just uncomment the include line from “…\Includes\SW_Modules\SW_Modules_Project\Project_Includes_Configuration.cin”

## Slide 4
2.1 PSM.vsysvar
  Import to CANoe configuration: (1) Environment → (2) System Variables → (3) Select File → (4 & 5) Open
1
2
3
4
5

## Slide 5
2.1 CORE_Functions_SysVar.vsysvar
  Location: e:/MKSProjects/SWVR_PP_CI_Activities/CANOE_TEST_PLATFORM/Includes/SW_Modules/SW_Modules_Core
  Import to CANoe configuration: (1) Environment → (2) System Variables → (3) Select File → (4 & 5) Open
1
2
3
4
5

## Slide 6
3. PSM.can
  Add to CANoe:
    (1) Simulation → (2) Simulation Setup → (3) Right click anywhere on the BUS → Insert CAPL test module
    Right click the new generated test module → (4) Configuration → (5) Test report → (6) Uncheck ‘Enable test report generation’
1
2
3
4
6
5

## Slide 7
    Common -> (7) Rename the module → (8) Attach test module trigger: sysPSM → (9) File… -> Attach test script: PSM.can
7
8
9

## Slide 8
4. PowerSupplyPannel.xvp
  Import to CANoe configuration: Home → Panel → Add Panel…
1
2
3
4

## Slide 9
4. PSM_StartValues.svc
  Import to CANoe configuration: (1) Environment→ (2) Start Values→ (3) Append (+) → (4) Open PSM_StartValues.svc
  IMPORTANT: Save the CANoe configuration before starting the simulation.
  The panel is configured through the ‘Start Values’ panel. Configuration is done before simulation start:
1
2
3
4

## Slide 10
Saving More Lives