## Slide 1: CANoe DMM implementation
More Lives Saved
More Life Lived
Victor Ursache
SWV

## Slide 2: 1. Needed files:
1.1 DMMargs.pyw && USBMultimeter.py → Functions for USB communication with DMM
1.2 DMMControl.cin → Functions for CAPL scripts
1.3 DMM.vsysvar → System variables
1.4 DigitalMultimeterPanelControl.can && DMMNode.can → Panel control functions / event (button) handlers
1.5 DigitalMultimeterPanel.xvp → Panel interface
1.6 sMeasureFile.txt → DMMoutput file
PTC location: e:/MKSProjects/SWVR_PP_CI_Activities/CANOE_TEST_PLATFORM/Includes/HW_Modules/DMM/
Implemented and tested on : CANoe Build 15.4.35 (SP4) – 64 bit

## Slide 3
1.1 DMMargs.pyw && USBMultimeter.py
  DMMargs.pyw: filePath and _sMultimeter should be updated if they were changed;
  USBMultimeter.py: should be added in the same file as DMMargs.pyw;
1

## Slide 4
1.2 DMMControl.cin
  If you wish to access DMM functionality through CAPL scripts, this must be included, otherwise skip this step.
    E.g., for DAIMLER MMA:

## Slide 5
1.3 DMM.vsysvar
  Import to CANoe configuration: Environment → System Variables → Select File → Open → Apply → OK
  Also, be sure that checkbox from is checked.
1
2
3
4
5
6
7
*
*

## Slide 6
1.4 DMMNode.can
  Add to CANoe:
    Simulation → Simulation Setup → Right click on BUS → Insert Network Node
    Right click the new generated node → Configuration → File → Open DMMNode.can
1
2
3
4
5

## Slide 7
1.4 DigitalMultimeterPanelControl.can
  Add to CANoe:
    Test→ Test Setup → Right click on the bottom of Test Setup for Test Modules → Open Test Environment → Project Functions.tse (pay attention: this *.tse file will add also other features like TMP or PowerSupply);
1
2
3
4

## Slide 8
1
2
3
4
4
1.5 DigitalMultimeterPanel.xvp
  Import to CANoe configuration: Home → Panel → Add Panel… → DigitalMultimeterPanel.xvp
  After : 1. Terminals: reads the actual settings: FRONT or REAR (if error shows ERROR);
                2. DCV button: reads the actual DC voltage;
                3. DCI button: reads the actual DC current;
                4. ACV button: reads the actual AC voltage;
                5. ACI button: reads the actual AC current;
                6. TEMP button: reads the actual 1xTemperature;
                7. 10 TEMPs button: reads the actual 10xTemp (only one DMM has this HW extension);
                8. Conversion Factor input: used to read current/voltage in the wright measure unit;
                9. All info will be shown on ‘DMM Output’.

## Slide 9
1.6 sMeasureFile.txt
  sMeasureFile.txt is the DMM output file. This file can be created manually or *.py file will create this file automatically (modify the filePath as you need and _sMultimeter);
1
2

## Slide 10
Saving More Lives