## Slide 1: CANoe FIB implementation
More Lives Saved
More Life Lived
Agapi Grigore
SWV

## Slide 2: 1. Needed files:
1.1 FIB_CANOE_DLL.dll → Functions for USB communication with FIB
1.2 FIB_Control.cin → Functions for CAPL scripts
1.3 FIB.vsysvar → System variables
1.4 FIB_Panel.can → Panel control functions / event (button) handlers
1.5 FIB.xvp → Panel interface
  + “Images” folder: Time_symbol.png + Voltage_symbol.png
1.6 Optional: FIB_Check folder → FIB check test
PTC location: e:/MKSProjects/SWVR_PP_CI_Activities/CANOE_Test_PLT/CANOE_FIB_Implementation
Implemented and tested on : CANoe Build 15.3.89 (SP3) – 64 bit

## Slide 3
1.1 FIB_CANOE_DLL.dll
  Add to CANoe configuration: File → Options → Programming → CAPL DLL → Add to “Simulation Setup / Test Setup”
1
2
3
4

## Slide 4
1.2 FIB_Control.cin
  If you wish to access FIB functionality through CAPL scripts, this must be included, otherwise skip this step.
    E.g., for DAIMLER MMA:
  Only use the functions present in FIB_Control.cin module. Do NOT use the .DLL functions directly (functions that start with “FIB_...”).
    Reason: FIB_Control.cin functions contain mandatory pre-checks e.g., check if a different fault is already active, etc.
FIB_Control.cin
(ok to use)
FIB_CANOE_DLL.dll
(do not use)

## Slide 5
1.3 FIB.vsysvar
  Import to CANoe configuration: Environment → System Variables → Select File → Open
1
2
3
4
5

## Slide 6
1.4 FIB_Panel.can
  Add to CANoe:
    Simulation → Simulation Setup → Right click on BUS → Insert Network Node
    Right click the new generated node → Configuration → File → Open FIB_Panel.can
1
2
3
4
5

## Slide 7
1.5 FIB.xvp
  Import to CANoe configuration: Home → Panel → Add Panel…
  FIB panel images will be displayed at runtime if the “Images” folder is in the same folder containing FIB.xvp e.g.,
    ..\Panels\FIB.xvp
    ..\Panels\Images\Time_symbol.png
1
2
3
4

## Slide 8: 2. FIB check
A successful connection is indicated by the message: “OK. FIB Channel count: ‘your channel count’ “ after starting the simulation.

## Slide 9
The test from ‘FIB_Check’ folder can be used to verify that the following FIB commands function properly for all channels: Open Circuit, Short to VCC, Short to GND, Set DAC Voltage, Restart_Board, Reset_Channel.
Please disconnect anything connected to the FIB output channels prior to running this test!
Test → Test Setup → Right click in test setup → Open Test Environment → Open FIB_Check.tse
1
2
3
4

## Slide 10
Double click on FIB_check → Run
Execution should last <2 min and a pass result looks like this
5
6

## Slide 11
Saving More Lives